## Slide 1: Network Access Control Systems at Educational Institutions
Richard Becker
Brian Leslie
Kansas State University

## Slide 2: Definition of “NAC,” Network Access Control
Authentication. (Allows users/devices access based on credentials or device type.)
End-point security. (Device is responsible for its own security.)
Access Control. (Differentiating access.)

## Slide 3: Kansas State has provided NAC for campus residents for the last six years, placing it ahead of many peer institutions.

## Slide 4: Special NAC criteria at an educational institution:
Network environment is implicitly somewhat insecure.
Extremely heterogeneous pool of computers and devices.
“False negatives” (devices that fail NAC tests and are blocked) lead to users reacting very impatiently; “false positives” (devices improperly passed through) are relatively harmless.

## Slide 5: General criteria for choosing a NAC solution:
Long-term viability and continued focus of vendor.
Interoperability with existing equipment.
Pricing structure.
Ease of implementation.
Getting accurate customer feedback (not necessarily from vendor’s sales team!).

## Slide 6: General criteria for choosing a NAC solution (continued):
Granularity of control.
Scalability. (To network load, and to different areas of enterprise.)
Ambitiousness of control. (E.g., does NAC use VLAN’s to control access.)
Fail-state (in-line or out-of-line?).

## Slide 7: General criteria for choosing a NAC solution (continued):
Detection of rogue devices (especially NAT-ed).
Ease of creating custom policies.
Easy, intuitive remediation. (Does user get clear instructions?)

## Slide 8: In general, our experience is that choosing between multiple NAC solutions is extremely difficult and time-consuming.
"The products bear very little similarity to one another... There's no such thing as 'best of breed' in NAC, because for the 12 vendors we evaluated, there are nearly 12 different 'breeds' of NAC product. " (Network World, 5-24-2010)

## Slide 9: Bradford vs. Impulse
In-line and out-of-line
Network topology requirements
Knowledge of edge devices
Fundamentals of operation
Support of NAC hardware

## Slide 10: In-line vs. Out-of-line
Implications
  Failure modes
    Bradford implemented with HA pair
    Impulse fails, allowing traffic
  Performance
  Hardware requirements
  Scalability

## Slide 11: Network Topology
Bradford
  Can be installed “anywhere” on the network
    Must be able to receive SNMP traps and access network devices via SSH
    Management and enforcement pair
  Enforcement at layer 2
  Handles DHCP/DNS for Registration, Remediation, and Quarantine vlans
  Recommended numbers of active clients

## Slide 13: Network Topology
Impulse SafeConnect
  Needs to be routed by device for which it is providing enforcement
  If Nat’ing is in use, it must be outside of enforcement scope
  Requires use of netflow
    Hardware support
  Can be a single enforcer or multiple enforcers
  Enforcement at layer 3

## Slide 15: Knowledge of Edge Devices
Bradford
  Must have control of edge network devices
    Dependency on supported devices
    Configuration management
      Syncing vlans and switch port status
      Misconfigured ports and enforcement
  What about unmanaged switches, hubs?

## Slide 16: Knowledge of Edge Devices
Impulse SafeConnect
  “Doesn’t care” what edge device is
    NAT’ing implications

## Slide 17: Fundamentals of Operation
Bradford
  Operates at layer 2
  Handles DHCP and DNS for Registration, Remediation, and Quarantine vlans
  Receives SNMP traps as clients attach, or radius requests for wireless
  Uses SSH to network devices for enforcement
  Persistent Agent vs. Run-once
  Policy enforcement and scheduled scans

## Slide 18: Fundamentals of Operation
Impulse SafeConnect
  Operates at layer 3
  Uses netflow exports from router for client detection
  Uses policy-based routing for enforcement
  Policy key vs. Non-policy key devices
  Policy enforcement constantly

## Slide 19: Support of NAC Hardware
Bradford
  Most support falls on IT staff
    Configuration backups
    Monitoring system health
    Hardware replacement / upgrades
  On-line community support
  Tech support available to work through issues
  Software upgrades

## Slide 20: Support of NAC Hardware
Impulse SafeConnect
  Managed service
    System monitoring
    Impulse backs up configurations
    Device replacement
    Software upgrades
  Tech support covered by maintenance

## Slide 21: Kansas State's implementation of SafeConnect is based on these criteria:
Windows Computers
User Authentication (eID, eID password)
Windows Updates/Install Automatically - turned on, pointed to WSUS server
Campus antivirus (Trend Micro) turned on, definitions up-to-date
Windows Firewall turned on
Peer-to-Peer Detection

## Slide 22: Kansas State's implementation of SafeConnect is based on these criteria:
Apple Computers
User authentication
Campus antivirus (Trend Micro) turned on, definitions up-to-date
OS X ver.10.5 or higher

## Slide 23: Kansas State's implementation of SafeConnect is based on these criteria:
Linux Computers
(No compatible NAC agent software.)
User authentication

## Slide 24: Kansas State's implementation of SafeConnect is based on these criteria:
Mobile Devices (browser based)
User authentication
Misc. devices (Set-top media
streamers, HDTV's, VOIP, etc.)
No checks; should be auto-detected. May require "manual pass" by help desk if device is not recognized.

## Slide 25: SafeConnect may seem – and is! – simplistic.
Their philosophy is to check enough to maintain adequate security, but not to be over-ambitious.

## Slide 26: Ways to Subvert SafeConnect:
User agent string.
Flashing MAC address.
NATing behind Linux.
Removing policy key.
Using guest network.

## Slide 27: The most problematic of these, changing the user agent, takes 10 seconds in Chrome and Mozilla.

## Slide 28
SafeConnect’s stated philosophy is that “we worry about the 99% of users, rather than exerting maximum effort on the top 1%.”
This makes sense, considering…

## Slide 29: In broad terms, this user is more of a threat than a technically sophisticated user.

## Slide 30: Summarizing – Can We Recommend SafeConnect?

## Slide 31: We have enough excitement at K-State without the network blowing up…

## Slide 32: Please contact us for questions or feedback.
Richard Becker
rlb@k-state.edu
Brian Leslie
bdleslie@k-state.edu